IV.) Using of the KEIL - µVision 2 Development Tools:

- Step: – Install the Tool chain - here you can download the Keil Development Tools:

http://www.keil-compiler.de/c166/

Execute ek166v423.exe and choose C:\KeilDemo for the installation path

- Step: Start Keil µVision and open the DAvE Project

If you see an open project – close it: Project - Close Project

Project - Open Project

choose: C:\e10k

choose: File type: Dave Project Files

choose: e10k.dpt

# Open

- Step: include the DAvE Header Files

mouse position: Files window: Dave Files: click right mouse button

## Add Files to Group ´Dave Files‘

input filename *.h

mark Asc0.h Cc1.h Io.h Main.h

# Add

do this 4 times:

Type: choose: Custom file

OK

Close

- Step: include the ConfPLL+Syscon3.c File

mouse position: Files window: User Files: click right mouse button

## Add Files to Group ´User Files‘

input filename *.c

mark ConfPLL+Syscon3.c

# Add

Close

- Step: Configure the Options for the Header Files:

right mouse button click Main.h

## Options for File Main.h

click ( Include in Target Build

click ( Always Build

click ( Link Publics Only

# OK

repeat this for the header files Cc1.h  Io.h  Asc0.h

- Step: Configure Compiler, Assembler, Linker, Locater, Hex-Converter and Build – Control:

right mouse button (Files window) click Target1

# Options for Target ´Target1‘

click ( Use On-chip XRAM

External Memory #1: select ROM, insert Start: 0x0C00000, insert Size: 0x20000

Output: click ( Create HEX File, choose HEX Format HEX-386(H167)

Listing (do nothing)

C166 (do nothing)

EC++ (do nothing)

A166 (do nothing)

L166 Locate (do nothing)

L166 Misc: insert Interrupt Vector Table Address 0x0C00000

Debug (do nothing)

# OK

- Step: Insert your application specific program:

double click MAIN.C and insert Global Variables:

char menu[] = "\r\n\n\n\n" "1 ... LED P9_P4 ON\r\n" "2 ... LED P9_P4 OFF\r\n" "3 ... LED P9_P4 blinking\r\n" " \r\n"; char question[] = "your choice: "; char message1[] = "\n\r*** LED is ON ***\r\n"; char message2[] = "\n\r*** LED is OFF ***\r\n"; char message3[] = "\n\r*** LED is BLINKING ***\r\n"; int wait=3; bit blinking=ON; char select=' ';

insert the function input()

char input (void) { char in=' '; do { printf(question); while (!ASC0_RIC_IR) _nop_(); ASC0_RIC_IR=0; in = ASC0_RBUF; }while (in!='1' && in!= '2' && in != '3'); return in; }

insert the following code in the main function:

Configure_PLL(); Configure_SYSCON3();

while(wait); while (1) { printf(menu); select=input(); switch (select) { case '1': blinking=OFF; P9_P4=LEDON, printf(message1); break; case '2': blinking=OFF; P9_P4=LEDOFF, printf(message2); break; case '3': blinking=ON, printf(message3); break; } }

double click Main.h and insert the following Defines:

#define OFF 0 #define ON 1 #define LEDON 0 #define LEDOFF 1

insert Global Variables

extern bit blinking; extern int wait;

insert Prototypes

extern void Configure_PLL (void); extern void Configure_SYSCON3 (void);

insert Includes (for printf() )

#include <stdio.h> #include <ctype.h>

double click ASC0.C

insert in the ASC0_vInit() function: (to start printf() )

ASC0_TIC_IR=1;

double click CC1.C

insert code for T0 interrupt service routine:

if(wait) wait--; if(blinking) P9_P4=~P9_P4;

- Step: Generate your application program – generate the hex file for Memtool:

Project

Rebuild all target files

Now you can close your project and µVision 2:

Project

Close Project

File

# Exit

Now you can program the hex output file e10k.H86 with Memtool in the OnChipFlash (Program Memory) of the XC164CS microcontroller.

- Step: using the simulator:

The uVision2 simulator has a couple of VTREG's that allow you the configuration of the reset behaviour. These pins of the Infineon XC16x are reflected by the following VTREGs: EA is the EA pin (0:= code fetch from external ROM ; 1:= code fetch from on-chip ROM) ALE is the ALE pin RD is the RD pin WR is the WR pin RSTCFGP are the levels on the configuration PINs NMIPIN is the NMI pin By default, the value of the EA pin is set to 0 to simulate the off-chip ROM. When this VTREG is 1 at CPU reset, the uVision2 simulates on-chip ROM and the RESET vector and interrupt vectors are at address 0xC00000. You can enable the on-chip ROM behaviour as described below: 1. Create a debugger INI file that contains the following commands: EA = 1 /* Start execution from on-chip ROM */ reset /* perform CPU reset: uses value at EA */ g, main /* execute program til main */ 2. Under Options for Target - Debug - Use Simulator, disable the option "Go till main ()" then enter the filename for the debugger INI file you created.

Start Keil µVision and open the Keil Project

If you see an open project – close it: Project - Close Project

Project - Open Project

choose: C:\e10k

choose: File type: Project Files (*.uv2)

choose: e10k.Uv2

## Open

## File – New

insert:

EA = 1 /* Start execution from on-chip ROM */ reset /* perform CPU reset: uses value at EA */ g, main /* execute program til main */

File – Save As...

choose: C:\e10k

## Dateiname/Filename: simulator.ini

## Speichern/Save

... include the simulator.ini File

mouse position: Files window: User Files: click right mouse button

## Add Files to Group ´User Files‘

input filename *.ini

mark simulator.ini

# Add

choose: Type: Custom file

# OK

Close

... configure the Options for the Simulator Ini-File:

Files window: right mouse button click simulator.ini

## Options for File simulator.ini

click ( Include in Target Build

click ( Always Build

click ( Link Publics Only

## OK

... configure Simulator – Control:

right mouse button (Files window) click Target1

# Options for Target ´Target1‘

# Debug

disable Go till main

insert Initialization File: simulator.ini

### OK

... using the simulator:

Debug

Start/Stop Debug Session

Debug

Go

View

Periodic Window Update

View

Serial Window #1

additionally – if you do not see the Serial Window #1:

View

Serial Window #1

Peripherals

I/O-Ports

Port9

Peripherals

Capcom1 (T0,T1)

T0